## Slide 1: The following program will be fed to the machine:
flw f1,34(t0) # f1=load float from Memory[t0+34]
flw f2,45(t1) # f2=load float from Memory[t1+45]
fmul.s f3,f2,f4 # f3=f2*f4
fsub.s f5,f1,f2 # f5=f1-f2
fdiv.s f0,f3,f1 # f0=f3/f1
fadd.s f1,f5,f2 # f1=f5+f2
flw, fsub and fadd will take 2 clock cycles.
fmul will take 10 clock cycles.
fdiv instruction will take 30 clock cycles.

## Slide 2
Operands Bus
At clock cycle 0, before we begin executing, things are as depicted. Integer registers t0=42 and t1=45. FP register F4 is 2.2.
fadd.s f1,f5,f2
fdiv.s f0,f3,f1
fsub.s f5,f1,f2
fmul.s f3,f2,f4
flw f2,45(t1)
flw f1,34(t0)
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 
F2 | 
F3 | 
F4 | 2.2
F5 | 
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Operation Bus
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 0

## Slide 3
Operands Bus
The first float load instruction is sent to the Address Unit where the address will be calculated (34+42=76) and sent to the first free load buffer, which is marked as busy (red). The destination of this operation (register F1) is also marked as busy.
fadd.s f1,f5,f2
fdiv.s f0,f3,f1
fsub.s f5,f1,f2
fmul.s f3,f2,f4
flw f2,45(t1)
flw f1,34(t0)
76
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 
F2 | 
F3 | 
F4 | 2.2
F5 | 
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Operation Bus
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 1
1

## Slide 4
Operands Bus
The second float load instruction (flw) is sent to the Address Unit where the address will be calculated (45+45=90) and sent to the first free load buffer, which is marked as busy (red). The destination of this operation (register F2) is also marked as busy.
fadd.s f1,f5,f2
fdiv.s f0,f3,f1
fsub.s f5,f1,f2
fmul.s f3,f2,f4
flw f2,45(t1)
90
76
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 
F2 | 
F3 | 
F4 | 2.2
F5 | 
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Operation Bus
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 2
1
2

## Slide 5
Operands Bus
The first float load instruction (flw) is ready and its result is broadcast to all subscribers. In this case, register F1.
fadd.s f1,f5,f2
fdiv.s f0,f3,f1
fsub.s f5,f1,f2
fmul.s f3,f2,f4
90
76
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 0.454
F2 | 
F3 | 
F4 | 2.2
F5 | 
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Operation Bus
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 3
1
2
3

## Slide 6
Operands Bus
We are still in clock cycle 3. The fmul.s operation is ready to go through the pipeline to the first free multiply reservation station, but one of its operands (F2) is not ready yet, so we mark the reservation station as busy and waiting for the flw f2 operation. Destination register F3 is also marked as busy. In the load buffer, the completed load (flw f1,34(t0)) is marked as free.
fadd.s f1,f5,f2
fdiv.s f0,f3,f1
fsub.s f5,f1,f2
fmul.s f3,f2,f4
90
FMUL.S | FLW F2 | 2.2
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 0.454
F2 | 
F3 | 
F4 | 2.2
F5 | 
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Operation Bus
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 3
1
2
3

## Slide 7
Operands Bus
We advance to clock cycle 4. Register F1 is no longer busy. The second load operation is read from the memory into the Common Data Bus and sent to its destination register F2, but also to the first busy multiply Reservation Station, since that Reservation Station is subscribed too.
fadd.s f1,f5,f2
fdiv.s f0,f3,f1
fsub.s f5,f1,f2
90
FMUL.S | 1.61 | 2.2
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 0.454
F2 | 1.61
F3 | 
F4 | 2.2
F5 | 
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Operation Bus
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 4
1
2
3
4
3

## Slide 8
Operands Bus
We are still in clock cycle 4. The fsub instruction continues down the pipeline. This substraction operation doesn't have all its operands since register F2 is still busy (the flw f2 ends this cycle) and, we consider, it wasn't subscribed in time for the earlier Common Data Bus broadcast, so we mark that addition Reservation Station as busy and waiting for register F2 load operation. Destination register F5 is marked as busy. The Load Buffer is empty since the second load (flw f2,45(t1)) ended.
fadd.s f1,f5,f2
fdiv.s f0,f3,f1
fsub.s f5,f1,f2
FSUB.S | 0.454 | FLW F2
FMUL.S | 1.61 | 2.2
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 0.454
F2 | 1.61
F3 | 
F4 | 2.2
F5 | 
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Operation Bus
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 4
1
2
3
4
3
4

## Slide 9
Operands Bus
We in clock cycle 5. Register F2 is no longer busy, so its value is sent to the adding Reservation Station waiting for it.
fadd.s f1,f5,f2
fdiv.s f0,f3,f1
FSUB.S | 0.454 | 1.61
FMUL.S | 1.61 | 2.2
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 0.454
F2 | 1.61
F3 | 
F4 | 2.2
F5 | 
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Operation Bus
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 5
1
2
3
4
3
4

## Slide 10
Operands Bus
Still in cycle 5, both the FSUB and FMUL in the reservation stations may begin executing. They are sent to the FP Adders/Multipliers.
fadd.s f1,f5,f2
fdiv.s f0,f3,f1
FSUB.S | 0.454 | 1.61
FMUL.S | 1.61 | 2.2
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 0.454
F2 | 1.61
F3 | 
F4 | 2.2
F5 | 
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Operation Bus
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 5
1
2
3
4
3
4

## Slide 11
Operands Bus
Still in cycle 5, the fdiv.s operation continues down the pipeline. We will need one more cycle to mark the occupied Reservation Stations as free, so we send this fdiv to the next free one. The fdiv.s must wait for the fmul.s operation, since it needs F3. We also need to mark its destination register, F0, as busy.
fadd.s f1,f5,f2
fdiv.s f0,f3,f1
FSUB.S | 0.454 | 1.61
FMUL.S | 1.61 | 2.2
FDIV.S | FMUL.S | 0.454
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 0.454
F2 | 1.61
F3 | 
F4 | 2.2
F5 | 
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Operation Bus
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 5
1
2
3
4
3
4
5

## Slide 12
Operands Bus
In clock cycle 6 the Reservation Stations for FMUL and FSUB are free, since they were sent to execute. Registers F3, F5 and F0 are still busy waiting for FMUL, FSUB and FDIV. The fadd f1 instruction continues down the pipeline to the first free adding Reservation Station. This instruction needs the results of the F5 register, that is waiting for the fsub.s operation to end, so we mark the Reservation Station as busy and waiting for fsub.s. We mark F1 as busy waiting for the fadd.s operation to complete.
fadd.s f1,f5,f2
FADD.S | FSUB.S | 1.61
FDIV.S | FMUL.S | 0.454
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 0.454
F2 | 1.61
F3 | 
F4 | 2.2
F5 | 
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Operation Bus
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 6
1
2
3
4
3
4
5
6

## Slide 13
Operation Bus
Operands Bus
In clock cycle 7 the fsub.s f5,f1,f2 has ended (it takes 2 cycles), so its results are sent from the FP Adders to the Common Data Bus and all elements waiting for it, like the only FADD in the adding Reservation Stations and the F5 register.
FADD.S | 1.156 | 1.61
FDIV.S | FMUL.S | 0.454
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 0.454
F2 | 1.61
F3 | 
F4 | 2.2
F5 | 1.156
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 7
1
2
3
4
3
4
5
6
7

## Slide 14
Operation Bus
Operands Bus
In clock cycle 8 the fadd.s f1,f5,f2 is sent to the FP Adders. Register F5 is no longer busy waiting.
FADD.S | 1.156 | 1.61
FDIV.S | FMUL.S | 0.454
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 0.454
F2 | 1.61
F3 | 
F4 | 2.2
F5 | 1.156
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 8
1
2
3
4
3
4
5
6
7

## Slide 15
Operation Bus
Operands Bus
We are in clock cycle 9. The fadd operation was sent to the FP Adders in the earlier cycle, so its Reservation Station is free. Since it takes 2 cycles for an add, Its results are written to the Common Data Bus and all subscribers, like, register F1.
FDIV.S | FMUL.S | 0.454
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 2.766
F2 | 1.61
F3 | 
F4 | 2.2
F5 | 1.156
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 9
1
2
3
4
3
4
5
6
7

## Slide 16
Operation Bus
Operands Bus
We are in clock cycle 10, register F1 is no longer busy.
FDIV.S | FMUL.S | 0.454
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 2.766
F2 | 1.61
F3 | 
F4 | 2.2
F5 | 1.156
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 10
1
2
3
4
3
4
5
6
7
9

## Slide 17
Operation Bus
Operands Bus
We are in clock cycle 14. The fmul operation has ended and its results are broadcast to the Common Data Bus and all its subscribers, that is, F3 register and the FDIV operation in the Reservation Station.
FDIV.S | 3.542 | 0.454
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 2.766
F2 | 1.61
F3 | 3.542
F4 | 2.2
F5 | 1.156
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 14
1
2
3
4
3
4
5
6
7
9
14

## Slide 18
Operation Bus
Operands Bus
We are in clock cycle 15. The fdiv.s operation has been sent to the FP Multipliers. Register F3 is no longer busy.
FDIV.S | 3.542 | 0.454
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 2.766
F2 | 1.61
F3 | 3.542
F4 | 2.2
F5 | 1.156
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 15
1
2
3
4
3
4
5
6
7
9
14

## Slide 19
Operation Bus
Operands Bus
Cycle 16. The Reservation Station containing the fdiv.s operation has been marked free.
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 
F1 | 2.766
F2 | 1.61
F3 | 3.542
F4 | 2.2
F5 | 1.156
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 16
1
2
3
4
3
4
5
6
7
9
14

## Slide 20
Operation Bus
Operands Bus
We are in clock cycle 44. The fdiv.s operation has ended and its results are sent to the Common Data Bus and all its subscribers, which is only F0.
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 7.8017
F1 | 2.766
F2 | 1.61
F3 | 3.542
F4 | 2.2
F5 | 1.156
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 44
1
2
3
4
3
4
5
6
7
9
14
44

## Slide 21
Operation Bus
Operands Bus
We are in clock cycle 45. F0 register is marked as free.
Instruction Unit
Memory Unit
Address Unit
Store
Buffer
Load
Buffer
Reservation
Stations
F0 | 7.8017
F1 | 2.766
F2 | 1.61
F3 | 3.542
F4 | 2.2
F5 | 1.156
Instruction Queue
FP Registers
FP Adders
FP Multipliers
Common Data Bus
flw f1,34(t0)
flw f2,45(t1)
fmul.s f3,f2,f4
fsub.s f5,f1,f2
fdiv.s f0,f3,f1
fadd.s f1,f5,f2
Issued
Finished
Clock Cycle: 45
1
2
3
4
3
4
5
6
7
9
14
44